## Slide 1: T2 Active stereopsis Task 2.1 Network Paradigm for Intelligent Vergence Control Task 2.2 3D description through interactive visual stereopsis adaptation
KATHOLIEKE UNIVERSITEIT LEUVEN
Laboratorium voor Neuro- en Psychofysiologie
Computational Neuroscience Research Group
07-08 March 2008
EYESHOTS project, Kick-off meeting
Bologna, Italy
Marc M. Van Hulle Nikolay Chumerin Karl Pauwels
Notes: Tutorial title: Active stereopsis
Problem to be tackled:
Task 2.1 Convolutional network for vergence control
goal: vergence control of mechatronic eye system, possibly conditioned with “attention”
- reflex-like vergence:
  system: eye movements are simulated (off-line), develop a network to estimate vergence given fixation point (or range), given limited set of near- and far disparity detectors
  output: retinocentric disparity map, vergence signal
  development: off-line using a simulator on-line with mechatronic eye system
- voluntary exploration:
  system: eye movements are simulated (off-line), train a convolutional network with an "attention" signal (locating and recognizing objects, from WP3)
  output: retinocentric disparity map, vergence signal in the presence of "attention" signal
  development: off-line using a simulator on-line with mechatronic eye system
----------
Task 2.2 3D description through interactive visual stereopsis adaptation
goal: explore/develop scanning strategies to accurately describe the 3D structure (or headcentric disparity) of a visual fragment by precise, near-tuned disparity detectors
subgoal: obtain a very accurate description, given disparity-detectors used are more precise than motor system
system: algorithmic developments to make transformation (from disparity to depth) robust to limited accuracy of motor system, e.g., insensitive to effects (on disparity) of small vergence/version errors (cf. Van Ee and Erkelens, 1996) vertical disparities will be exploited to obtain more accurate eye position information (Read and Cumming, 2006)-----
Necessary background:
expertise in computer and biological vision, cell and systems modeling, neural networks, self-organization and adaptive control, machine learning

## Slide 2: Overview
Tasks description
Proposed approach
Background
Simulator
Notes: As reported in the minutes of the warm-up meeting, "the tutorials [T1, ..., T7] should be intended as detailed presentations (50 min) by each partner on
  the problem tacked,
  the necessary background,
  the approach one intends to follow,
  how the approach (and expected results) fits with other project's components".
Hence, I expect they will be given by WP leaders and/or their collaborators.

## Slide 3: Task 2.1 description
Main goal
  develop a model of vergence control of mechatronic eye system, possibly conditioned with “attention”
Input
  Responses of population of disparity detectors
  “Attention” signal
Output
  Vergence control signal
  Learned sparse coding
  Learned control strategy
Notes: Tutorial title: Active stereopsis
Problem to be tackled:
Task 2.1 Convolutional network for vergence control
goal: vergence control of mechatronic eye system, possibly conditioned with “attention”
- reflex-like vergence:
  system: eye movements are simulated (off-line), develop a network to estimate vergence given fixation point (or range), given limited set of near- and far disparity detectors
  output: retinocentric disparity map, vergence signal
  development: off-line using a simulator on-line with mechatronic eye system
- voluntary exploration:
  system: eye movements are simulated (off-line), train a convolutional network with an "attention" signal (locating and recognizing objects, from WP3)
  output: retinocentric disparity map, vergence signal in the presence of "attention" signal
  development: off-line using a simulator on-line with mechatronic eye system
----------
Task 2.2 3D description through interactive visual stereopsis adaptation
goal: explore/develop scanning strategies to accurately describe the 3D structure (or headcentric disparity) of a visual fragment by precise, near-tuned disparity detectors
subgoal: obtain a very accurate description, given disparity-detectors used are more precise than motor system
system: algorithmic developments to make transformation (from disparity to depth) robust to limited accuracy of motor system, e.g., insensitive to effects (on disparity) of small vergence/version errors (cf. Van Ee and Erkelens, 1996) vertical disparities will be exploited to obtain more accurate eye position information (Read and Cumming, 2006)-----
Necessary background:
expertise in computer and biological vision, cell and systems modeling, neural networks, self-organization and adaptive control, machine learning

## Slide 4: Task 2.2 description
Main goal
explore/develop scanning strategies to accurately describe the 3D structure (or headcentric disparity) of a visual fragment by precise disparity detectors
Subgoal
make transformation (from disparity to depth) robust to limited accuracy of motor system, e.g., insensitive to effects (on disparity) of small vergence/version errors (cf. Van Ee and Erkelens, 1996)
Output
a very accurate fragment description, given disparity-detectors used are more precise than motor system

## Slide 5: Necessary background
Expertise in computer and biological vision, cell and systems modeling, neural networks, self-organization and adaptive control, machine learning

## Slide 6: Task 2.1 description (cont.)
Assumptions:
  “Head” is fixed (orientation is fixed, baseline is constant)
  Gaze direction is fixed in 3-D (on the object, which is not necessary at the fixation point yet)

## Slide 7: Task 2.1 description (cont.)
With fixed head and its gaze direction vergence has one degree of freedom, and though could be controlled by one parameter:
or
Vergence angle
Distance to the fixation point

## Slide 8: Proposed model
Cameras
S-cells bank (3D band-pass Gabor-like channels)
C-cell disparity detectors
Disparity-based feature detectors
Convolutional network
Vergence control
Sparse coding
Object recognition
Reaching
Attention

## Slide 9: Convolutional Networks
LeNet 5 Used in digits/character recognition
Y. LeCun, L. Bottou, Y. Bengio, and P. Haffner. Gradient-based learning applied to document recognition. Proceedings of the IEEE, November 1998.
LeNet 7 Used in generic object recognition

## Slide 10: Convolutional Networks
Modified LeNet 5
Y. LeCun, L. Bottou, Y. Bengio, and P. Haffner. Gradient-based learning applied to document recognition. Proceedings of the IEEE, November 1998.
64×64
60×60×10
C-layer 10 kernels (5×5)
5×5
30×30×10
2×2
S-layer (2×2)
26×26×16
C-layer 64 kernels (5×5)
S-layer: (2×2)
13×13×16
1×1×180
1×1×7
C-layer: 2880 kernels (13×13)
F-layer

## Slide 11: Vergence Strategies
General purpose strategy
aims to maximize the total activity of the retinocentric map of ‘C-cell’ disparity detectors in as few vergence steps as possible)
starting from a fixation point and an initial vergence, we have a ‘basic’ disparity cells activity pattern
the network outputs a new vergence estimate that, when applied increases this activity pattern, which produces a new vergence estimate, etc., until convergence
Specific for object detection strategy
the top-down signal that binds the visual fragments based on attention/selection indicates which descriptors of the fragment are most conspicuous
the activity pattern of these descriptors is maximized by iterating on the vergence much as in the previous general purpose strategy

## Slide 12: Vergence Network Types
Reflex-like vergence
No “attention” input signal.
Two steps of network development:
Training phase (eye movements are simulated, current vergence as additional input, output disparity detectors tuning is constraint to a limited number of detectors)
Testing phase (on real robot eye setup, looking on effect of learning at different levels of the network architecture)
Voluntary exploration
Extra input signal attention coming from the saliency map developed in WP3.

## Slide 13: List of deliverables
D2.1 Convolutional network for vergence control. Technical report. (Month 18, preliminary report, Month 30 final report)
D2.2a Algorithm for 3D scene description through interactive visual stereopsis adaptation using a conventional binocular vision platform. Software module. (Month 24)
D2.2b Algorithm for 3D scene description through interactive visual stereopsis adaptation using the mechatronic system. Technical report and Demonstrator. (Month 36)

## Slide 14: Simulator
In order to “dive into the problem” we have developed a simulator which consists of:
Robotic head model
Environment model
Ray-tracing rendering engine
Applications of the simulator:
Database of scenes and high quality synthetic stereo images for further off-line training
Precise estimates of the horizontal and vertical disparities, optical flow
On-line modeling and training (?)

## Slide 15: Robotic head model
A model of the robotic head has been developed. In the model one can precisely control all important parameters:
Head position
Head orientation (which includes gaze direction)
Vergence of the “eyes” (by means of vergence angle or distance to the fixation point)
And so on…

## Slide 16: Environment model

## Slide 17: Ray-tracing rendering engine
As existing ray tracers do not give access to internal data we have developed our own ray-tracing engine in MATLAB environment.
The engine allows to obtain:
  High-quality “eye views”: synthetic images (textures, lights, anti-aliasing)
  Precise horizontal and vertical disparities
  Precise optical flow

## Slide 18: Ray-tracing rendering engine

## Slide 19: Disparity revelations…
Vertical disparity weakly depends on scene structure except for some extreme cases
Vertical disparity

## Slide 20: Disparity revelations…
Only one case, when vertical disparity is almost zero and does not depend on the scene is the case of zero-verged eyes with gaze direction orthogonal to the baseline.
10-14 = almost zero

## Slide 21: Simple disparity-based vergence technique